NOTICE:

- The figures here are for reference only and may have differences with the actual product you received, however they share the same assembly way.

- Please read the instruction completely for easy installation, which will also help you to avoid scratches or other potential damages to your appealing car.

- Please periodically check and retighten all the hardware and clean the investment for a refresh look.

PARTS LIST:

| No. | Name | Qty | Remarks | No. | Name | Qty | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | DOS shell | 2 |  |  | Plastic screw | 10 |  |
|  | Support body | 2 |  |  | Plastic plug | 4 |  |
|  | Cover board | 2 |  |  | Flange bolt | 10 | M6x20 |
|  | Stock sticker | 2 |  |  | Hex nut | 20 | M6 |
|  | Rear bracket | 2 |  |  | Enlarge washer | 20 | 6mm |
|  | Front bracket | 2 |  |  | Philips head screw | 10 | ST4.8x30 |
|  | Flange nut | 14 |  |  | Enlarge washer | 10 | 5mm |
|  | Bolt Clip | 12 |  |  |  |  |  |

ASSEMBLY PROCEDURE:

Step 1：Check all the contents are available in accordance with the above list.

Step 2：Install the hardware  on , do not tighten all hardware. Note: the big hole need upwards.(Fig.1, fig.2)

Step 3：Install 4 hardware in vehicle bottom.(Fig.3, fig.4)

Step 4：Remove the car around parts till fig.5 showing.

Step 5：Install the hardware on vehicle as fig.6 showing, and then tighten the nuts.

Step 6：Install the  in vehicle bottom using  as fig.7-10 showing. Note: one side of need to insert in  as fig.8 showing.

Step 7：Open the door, then install the DOS shell on vehicle, fix the appropriate position, pat the buckle to fasten the DOS shell. (fig.11) Note: when install the front, the DOS shell need install on outside of factory fender.

Step 8：When install the rear of DOS shell, you need insert the factory fender between DOS shell and Stock sticker. (fig.12)

Step 9：Install the hardware, A total of 10. (fig.13)

Step 10：Fasten the running board using the hardware as fig.14 showing.

Step 11：Test and make sure that the running board is steadily fixed, and then tighten all the hardware .

Step 12：Repeat step 2-11 for other side running board.

Step 13：Verify that all the hardware was installed and fully tightened.

DISCLAIMER: We are not responsible for any quality problems caused by improper installation and use.

# Text boxes

Fig.1

Rear bracket

Front bracket

Fig.2

Big hole

Big hole

Support body

Support body

Fig.4

Fig.3

Plastic plug

Plastic plug

Fig.6

Fig.5

Install the support body.

Fig.8

Fig.7

Install the cover board

Fig.10

Fig.9

Fig.11

Fasten the buckle to vehicle

Note：This face need to install in outside of factory fender

Fig.12

Stock sticker

DOS shell

Fig.14

Fig.13